Diphenyl guanidine

Company Information

Sunchem Co.,Ltd.

Add: A-11F, 186 Yangtzi Middle Road, Yangzhou, China.

Tel:+86 514 87851548

Fax:+86 514 87872867

Email: info@sunchemgroup.com

| Product Identification |  |
| --- | --- |
| 【Product Name】 1,3-Diphenylguanidine |
| 【Synonyms】 1,2-Di(phenyl)guanidine Denax Melaniline N,N'-Diphenylguanidine sym-Diphenylguanidine Vulkazit |
| 【CAS】 102-06-7 |
| 【Formula】 C13H13N3 |
| 【Molecular Weight】 211.29 |
| 【EINECS】 203-002-1 |
| 【RTECS】 MF0875000 |
| 【RTECS Class】 Tumorigen; Mutagen; Reproductive Effector |
| 【Merck】 13,3356 |
| 【Beilstein/Gmelin】 1875653 |
| 【Beilstein Reference】 4-12-00-00769 |
| 【EC Index Number】 612-149-00-4 |
| 【EC Class】 Toxic for reproduction Category 3; Harmful; Irritant; Dangerous for the Environment |

| Physical and Chemical Properties |  |
| --- | --- |
| 【Appearance】 White to cream-colored chalky powder. Bitter taste and slight odor. |
| 【Solubility in water】 Soluble |
| 【Melting Point】 146 - 147 |
| 【Boiling Point】 321 |
| 【Vapor Pressure】 0.0003 (25 C) |
| 【Density】 1.19 g/cm3 (20 C) |
| 【pKa/pKb】 3.58 (pKb) |
| 【Partition Coefficient】 2.36 |
| 【Heat Of Vaporization】 56.3 kJ/mol |
| 【Usage】 Primary material for standardizing acids, free base & phthalate as accelerators for vulcanization of rubber. |
| 【Vapor Density】 1.115 |

| First Aid Measures |  |
| --- | --- |
| 【Ingestion】 Do NOT induce vomiting. If victim is conscious and alert, give 2-4 cupfuls of milk or water. Never give anything by mouth to an unconscious person. Get medical aid. |
| 【Inhalation】 Remove from exposure to fresh air immediately. If breathing is difficult, give oxygen. Get medical aid. DO NOT use mouth-to-mouth respiration. If breathing has ceased apply artificial respiration using oxygen and a suitable mechanical device such as a bag and a mask. |
| 【Skin】 Get medical aid. Flush skin with plenty of soap and water for at least 15 minutes while removing contaminated clothing and shoes. Wash clothing before reuse. |
| 【Eyes】 Immediately flush eyes with plenty of water for at least 15 minutes, occasionally lifting the upper and lower eyelids. Get medical aid. |

| Handling and Storage |  |
| --- | --- |
| 【Storage】 Keep container closed when not in use. Store in a tightly closed container. Store in a cool, dry, well-ventilated area away from incompatible substances. |
| 【Handling】 Wash thoroughly after handling. Use only in a well ventilated area. Minimize dust generation and accumulation. Avoid contact with eyes, skin, and clothing. Keep container tightly closed. Avoid ingestion and inhalation. Wash clothing before reuse. |

| Hazards Identification |  |
| --- | --- |
| 【Inhalation】 May cause respiratory tract irritation. |
| 【Skin】 May cause skin irritation. May be absorbed through the skin. |
| 【Eyes】 Causes eye irritation. |
| 【Ingestion】 Harmful if swallowed. May cause irritation of the digestive tract. |
| 【EC Risk Phrase】 R 22 36/37/38 51/53 62 |
| 【EC Safety Phrase】 S 26 36/37/39 61 |
| 【UN (DOT)】 3077 |

| Exposure Controls/Personal Protection |  |
| --- | --- |
| 【Personal Protection】 Eyes: Wear appropriate protective eyeglasses or chemical safety goggles as described by OSHA's eye and face protection regulations in 29 CFR 1910.133 or European Standard EN166. Skin: Wear appropriate protective gloves to prevent skin exposure. Clothing: Wear appropriate protective clothing to prevent skin exposure. |
| 【Respirators】 A respiratory protection program that meets OSHA's 29 CFR 1910.134 and ANSI Z88.2 requirements or European Standard EN 149 must be followed whenever workplace conditions warrant a respirator's use. |
| 【Exposure Effects】 Reproductive effects have been reported in animals. Laboratory experiments have resulted in mutagenic effects. Repeated or prolonged exposure may cause allergic reactions in sensitive individuals. |
| 【Poison Class】 3 |

| Fire Fighting Measures |  |
| --- | --- |
| 【Flash Point】 148 |
| 【Fire Fighting】 Wear a self-contained breathing apparatus in pressure-demand, MSHA/NIOSH (approved or equivalent), and full protective gear. During a fire, irritating and highly toxic gases may be generated by thermal decomposition or combustion. Extinguishing media: Use extinguishing media most appropriate for the surrounding fire. In case of fire use water spray, dry chemical, carbon dioxide, or appropriate foam. |
| 【Fire Potential】 This chemical is combustible. |

| Accidental Release Measures |  |
| --- | --- |
| 【Small spills/leaks】 Clean up spills immediately, using the appropriate protective equipment. Sweep up, then place into a suitable container for disposal. Avoid generating dusty conditions. Provide ventilation. |

| Stability and Reactivity |  |
| --- | --- |
| 【Stability】 Stable under normal temperatures and pressures. |
| 【Incompatibilities】 Strong oxidizing agents. |
| 【Decomposition】 Nitrogen oxides, carbon monoxide, carbon dioxide, nitrogen. |

| Transport Information |  |
| --- | --- |
| 【UN Number】 3077 |
| 【HS Code】 2925 20 00 |